## Slide 1: Detection of Embedded Malware/Trojan in Hardware devices used in Power Sector
Cyber Sentinels_CSE

## Slide 2: Agenda
Hardware Trojans
Threats from Hardware Trojans
Our Solution Proposition Walkthrough

## Slide 3: Insights
Modern IC designs often involve third-party intellectual property (IP) cores because of the high design complexity, the restriction of time-to-market and the cost constraint of final products. One of the challenges faced by the IP reuse-based design methodology is the untrustworthiness of the outsourced IPs. It is convinced that there are opportunities in which the IP cores contain malicious extra logic, namely Hardware Trojan (HT). HTs can cause the circuit failure or leak confidential information, which raise serious concerns about trustworthiness of ICs used in Internet of Things (IoT) and consumer electronics (CE) , as well as mission critical applications.

## Slide 6
Action Mechanism of Hardware Trojan

## Slide 7
AES‐T1000
The Trojan leaks the secret key from a cryptographic chip running the AES algorithm through a covert channel.
The channel adapts the concepts from spread spectrum communications (also known as Code-Division Multiple Access (CDMA)) to distribute the leakage of single bits over many clock cycles.
The Trojan employs this method by using a pseudo-random number generator (PRNG) to create a CDMA code sequence, the PRNG initialized to a predefined value.
The code sequence is then used to XOR modulate the secret information bits. The modulated sequence is forwarded to a leakage circuit (LC) to set up a covert CDMA channel in the power side-channel.
The LC is realized by connecting eight identical flip-flop elements to the single output of the XOR gate to mimic a large capacitance
Trojan taxonomy
Insertion phase: Design
Abstraction level: Register Transfer level
Activation mechanism: Triggered Internally
Effects: Leak Information
Location: Processor
Physical characteristics: Functional

## Slide 8: Summary
We propose a HT detection method based on structural features of Trojans and host circuits. We extract a number of structural features of HTs from gate-level netlists and construct a HT database covering the combinational logic HT features and sequential logic HT features. Efficient feature analysis algorithms are developed to search small piece of circuits which match the features in the database and are assigned with a score. A score outlier determination algorithm is developed to identify suspicious Trojan elements. The experimental results show that the proposed method is capable of detecting all stealth Trojans from the benchmarks with short runtime and low false positive rate, compared to the existing HT detection methods.

## Slide 9: Thank You